## Slide 1: INTER-VLAN ROUTING
Routing on-a-stick

## Slide 2: Target
InterVLAN routing tra VLAN 10 e VLAN 20 tramite il router con una sola interfaccia ethernet

## Slide 3: STEP #1
PC’s addresses:
192.168.0.101/25
192.168.0.102/25
192.168.0.201/25
192.168.0.202/25

## Slide 4: STEP #2
VLAN
(switch, config mode)
VLAN 10
VLAN 20

## Slide 5: STEP #3
Port’s config
Access VLAN 10:
    Int fa0/1
    Int fa0/3
Access VLAN 20:
    Int fa0/2
    Int fa0/4
Trunk:
    Int fa0/24

## Slide 6: STEP #4: router’s config
Subinterfaces:
Encapsulation dot1Q
IP address
No shutdown
Router(config)# interface fastEthernet 0/0.10
Router(config-subif)# encapsulation dot1Q 10
Router(config-subif)#ip addr 192.168.0.100 255.255.255.0
Router(config)# interface fastEthernet 0/0.20
Router(config-subif)# encapsulation dot1Q 20
Router(config-subif)#ip addr 192.168.0.100 255.255.255.0
Router(config-subif)#exit
Router(config)# interface fastEthernet 0/0
Router(config-if)#no-shut

## Slide 7: STEP #5: PING...

## Slide 8: Extra: ripasso comandi DHCP